https://www.cloudskillsboost.google/course_sessions/2617047/labs/344865

# Multiple VPC Networks
## Overview
In this lab you create several VPC networks and VM instances and test connectivity across networks. Specifically, you create two custom mode networks (managementnet and privatenet) with firewall rules and VM instances as shown in this network diagram:

The mynetwork network with its firewall rules and two VM instances (mynet-eu-vm and mynet-us-vm) have already been created for you for this lab.

Objectives
In this lab, you will learn how to perform the following tasks:
- Create custom mode VPC networks with firewall rules
- Create VM instances using Compute Engine
- Explore the connectivity for VM instances across VPC networks
- Create a VM instance with multiple network interfaces

### Activate Cloud Shell
gcloud auth list
gcloud config list project

  - fact_checkQuiz
  Quiz
  - Video
    Activity completed
    Summary
## Keeping an eye on things
  - Video
    Introduction
  - Video
    Introduction to Infrastructure as Code (IaC)
  - Video
    Terraform
  - Video
    Monitoring and managing services, applications, and infrastructure
  - Video
    Google Cloud's operations suite
  - Video
    Lab Intro: Cloud Monitoring: Qwik Start
  - Lab
    Cloud Monitoring: Qwik Start
  - Quiz
    Quiz
  - Video
    Summary
  - Document
    Demonstrate your capabilities further!

- GSP211

- Overview
- Objectives
- Setup and requirements
- Task 1. Create custom mode VPC networks with firewall rules
- Task 2. Create VM instances
- Task 3. Explore the connectivity between VM instances
- Task 4. Create a VM instance with multiple network interfaces
- Congratulations!
# Multiple VPC Networks
1 hour 10 minutes5 Credits
## GSP211

## Overview
In this lab you create several VPC networks and VM instances and test connectivity across networks. Specifically, you create two custom mode networks (managementnet and privatenet) with firewall rules and VM instances as shown in this network diagram:

The mynetwork network with its firewall rules and two VM instances (mynet-eu-vm and mynet-us-vm) have already been created for you for this lab.
## Objectives
In this lab, you will learn how to perform the following tasks:
- Create custom mode VPC networks with firewall rules
- Create VM instances using Compute Engine
- Explore the connectivity for VM instances across VPC networks
- Create a VM instance with multiple network interfaces
## Setup and requirements
### Before you click the Start Lab button
Read these instructions. Labs are timed and you cannot pause them. The timer, which starts when you click Start Lab, shows how long Google Cloud resources will be made available to you.
This hands-on lab lets you do the lab activities yourself in a real cloud environment, not in a simulation or demo environment. It does so by giving you new, temporary credentials that you use to sign in and access Google Cloud for the duration of the lab.
To complete this lab, you need:
Access to a standard internet browser (Chrome browser recommended).
Note: Use an Incognito or private browser window to run this lab. This prevents any conflicts between your personal account and the Student account, which may cause extra charges incurred to your personal account.
Time to complete the lab---remember, once you start, you cannot pause a lab.
Note: If you already have your own personal Google Cloud account or project, do not use it for this lab to avoid extra charges to your account.
### How to start your lab and sign in to the Google Cloud Console
1. Click the Start Lab button. If you need to pay for the lab, a pop-up opens for you to select your payment method. On the left is the Lab Details panel with the following:
  1. The Open Google Console button
  2. Time remaining
  3. The temporary credentials that you must use for this lab
  4. Other information, if needed, to step through this lab
2. Click Open Google Console. The lab spins up resources, and then opens another tab that shows the Sign in page.
  Tip: Arrange the tabs in separate windows, side-by-side.
  Note: If you see the Choose an account dialog, click Use Another Account.
3. If necessary, copy the Username from the Lab Details panel and paste it into the Sign in dialog. Click Next.
4. Copy the Password from the Lab Details panel and paste it into the Welcome dialog. Click Next.
  Important: You must use the credentials from the left panel. Do not use your Google Cloud Skills Boost credentials.Note: Using your own Google Cloud account for this lab may incur extra charges.
5. Click through the subsequent pages:
  1. Accept the terms and conditions.
  2. Do not add recovery options or two-factor authentication (because this is a temporary account).
  3. Do not sign up for free trials.
After a few moments, the Cloud Console opens in this tab.
Note: You can view the menu with a list of Google Cloud Products and Services by clicking the Navigation menu at the top-left.
### Activate Cloud Shell
Cloud Shell is a virtual machine that is loaded with development tools. It offers a persistent 5GB home directory and runs on the Google Cloud. Cloud Shell provides command-line access to your Google Cloud resources.
Click Activate Cloud Shell  at the top of the Google Cloud console.
When you are connected, you are already authenticated, and the project is set to your PROJECT_ID. The output contains a line that declares the PROJECT_ID for this session:
Your Cloud Platform project in this session is set to YOUR_PROJECT_ID
gcloud is the command-line tool for Google Cloud. It comes pre-installed on Cloud Shell and supports tab-completion.
(Optional) You can list the active account name with this command:
gcloud auth list
Copied!
1. Click Authorize.
2. Your output should now look like this:
Output:
ACTIVE: *
ACCOUNT: student-01-xxxxxxxxxxxx@qwiklabs.net
To set the active account, run:
    $ gcloud config set account `ACCOUNT`
(Optional) You can list the project ID with this command:
gcloud config list project
Copied!
Output:
[core]
project = <project_ID>
Example output:
[core]
project = qwiklabs-gcp-44776a13dea667a6
Note: For full documentation of gcloud, in Google Cloud, refer to the gcloud CLI overview guide.
## Task 1. Create custom mode VPC networks with firewall rules
Create two custom networks managementnet and privatenet, along with firewall rules to allow SSH, ICMP, and RDP ingress traffic.
### Create the managementnet network
Create the managementnet network using the Cloud Console.
In the Cloud Console, navigate to Navigation menu () > VPC network > VPC networks.

1. Notice the default and mynetwork networks with their subnets.
  Each Google Cloud project starts with the default network. In addition, the mynetwork network has been premade as part of your network diagram.
2. Click Create VPC Network.
3. Set the Name to managementnet.
4. For Subnet creation mode, click Custom.
5. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Name	managementsubnet-us
Region	us-east1
IPv4 range	10.130.0.0/20

1. Click Done.
2. Click EQUIVALENT COMMAND LINE.
  These commands illustrate that networks and subnets can be created using the Cloud Shell command line. You will create the privatenet network using these commands with similar parameters.
3. Click Close.
4. Click Create.
#### Test Completed Task
Click Check my pr

### Create the privatenet network
Create the privatenet network using the Cloud Shell command line.
Run the following command to create the privatenet network:
gcloud compute networks create privatenet --subnet-mode=custom
Copied!
Run the following command to create the privatesubnet-us subnet:
gcloud compute networks subnets create privatesubnet-us --network=privatenet --region=us-east1 --range=172.16.0.0/24
Copied!
Run the following command to create the privatesubnet-eu subnet:
gcloud compute networks subnets create privatesubnet-eu --network=privatenet --region=europe-west1 --range=172.20.0.0/20
Copied!
#### Test Completed Task
Click Che
Run the following command to list the available VPC networks:
gcloud compute networks list
Copied!
The output should look like this:
Run the following command to list the available VPC subnets (sorted by VPC network):
gcloud compute networks subnets list --sort-by=NETWORK
Copied!
The output should loo
1. In the Cloud Console, navigate to Navigation menu > VPC network > VPC networks.
2. You see that the same networks and subnets are listed in the Cloud Console.
### Create the firewall rules for managementnet
Create firewall rules to allow SSH, ICMP, and RDP ingress traffic to VM instances on the managementnet network.
1. In the Cloud Console, navigate to Navigation menu () > VPC network > Firewall.
2. Click + Create Firewall Rule.
3. Set the following values, leave all other values at their defaults:
:
Property	Value (type value or select option as specified)
Name	managementnet-allow-icmp-ssh-rdp
Network	managementnet
Targets	All instances in the network
Source filter	IPv4 Ranges
Source IPv4 ranges	0.0.0.0/0
Protocols and ports	Specified protocols and ports, and then check tcp, type: 22, 3389; and check Other protocols, type: icmp.

Note: Make sure to include the /0 in the Source IPv4 ranges to specify all networks.
1. Click EQUIVALENT COMMAND LINE.
  These commands illustrate that firewall rules can also be created using the Cloud Shell command line. You will create the privatenet's firewall rules using these commands with similar parameters.
2. Click Close.
3. Click Create.
#### Test Completed Task
Click Check
### Create the firewall rules for privatenet
Create the firewall rules for privatenet network using the Cloud Shell command line.
In Cloud Shell, run the following command to create the privatenet-allow-icmp-ssh-rdp firewall rule:
gcloud compute firewall-rules create privatenet-allow-icmp-ssh-rdp --direction=INGRESS --priority=1000 --network=privatenet --action=ALLOW --rules=icmp,tcp:22,tcp:3389 --source-ranges=0.0.0.0/0
Copied!
The output should look like this:
Creating firewall...done.
NAME: privatenet-allow-icmp-ssh-rdp
NETWORK: privatenet
DIRECTION: INGRESS
PRIORITY: 1000
ALLOW: icmp,tcp:22,tcp:3389
DENY:
DISABLED: False
#### Test Completed Task
Click Check my progress to verify your perf
Run the following command to list all the firewall rules (sorted by VPC network):
gcloud compute firewall-rules list --sort-by=NETWORK
Copied!
The output should look like this:
NAME: default-allow-icmp
NETWORK: default
DIRECTION: INGRESS
PRIORITY: 65534
ALLOW: icmp
DENY:
DISABLED: False
NAME: default-allow-internal
NETWORK: default
DIRECTION: INGRESS
PRIORITY: 65534
ALLOW: tcp:0-65535,udp:0-65535,icmp
DENY:
DISABLED: False
...
The firewall rules for mynetwork network have been created for you. You can define multiple protocols and ports in one firewall rule (privatenet and managementnet), or spread them across multiple rules (default and mynetwork).
1. In the Cloud Console, navigate to Navigation menu > VPC network > Firewall.
2. You see that the same firewall rules are listed in the Cloud Console.
## Task 2. Create VM instances
Create two VM instances:
- managementnet-us-vm in managementsubnet-us
- privatenet-us-vm in privatesubnet-us
### Create the managementnet-us-vm instance
Create the managementnet-us-vm instance using the Cloud Console.
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
  The mynet-eu-vm and mynet-us-vm has been created for you, as part of your network diagram.
2. Click Create instance.
3. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Name	managementnet-us-vm
Region	us-east1
Zone	<filled in at lab start>
Series	E2
Machine type	e2-micro

1. From Advanced options, click Networking, Disks, Security, Management, Sole-tenancy dropdown.
2. Click Networking.
3. For Network interfaces, click the dropdown to edit.
4. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Network	managementnet
Subnetwork	managementsubnet-us

1. Click Done.
2. Click EQUIVALENT CODE.
  This illustrate that VM instances can also be created using the Cloud Shell command line. You will create the privatenet-us-vm instance using these commands with similar parameters.
3. Click Create.
#### Test Completed Task
Click Che
### Create the privatenet-us-vm instance
Create the privatenet-us-vm instance using the Cloud Shell command line.
In Cloud Shell, run the following command to create the privatenet-us-vm instance:
gcloud compute instances create privatenet-us-vm --zone="" --machine-type=e2-micro --subnet=privatesubnet-us
Copied!
The output should look like this:
Created [https://www.googleapis.com/compute/v1/projects/qwiklabs-gcp-04-972c7275ce91/zones/""/instances/privatenet-us-vm].
NAME: privatenet-us-vm
ZONE: ""
MACHINE_TYPE: e2-micro
PREEMPTIBLE:
INTERNAL_IP: 172.16.0.2
EXTERNAL_IP: 34.135.195.199
STATUS: RUNNING
#### Test Completed Task
Click Ch
Run the following command to list all the VM instances (sorted by zone):
gcloud compute instances list --sort-by=ZONE
Copied!
The output should look like this:
NAME: mynet-eu-vm
ZONE: europe-west1-a
MACHINE_TYPE: e2-micro
PREEMPTIBLE:
INTERNAL_IP: 10.164.0.2
EXTERNAL_IP: 34.147.23.235
STATUS: RUNNING
NAME: mynet-us-vm
ZONE: ""
MACHINE_TYPE: e2-micro
PREEMPTIBLE:
INTERNAL_IP: 10.128.0.2
EXTERNAL_IP: 35.232.221.58
STATUS: RUNNING
...
1. In the Cloud Console, navigate to Navigation menu () > Compute Engine > VM instances.
2. You see that the VM instances are listed in the Cloud Console.
3. Click on Column display options, then select Network. Click Ok.
  There are three instances in us-east1 and one instance in europe-west1. However, these instances are spread across three VPC networks (managementnet, mynetwork and privatenet), with no instance in the same zone and network as another. In the next section, you explore the effect this has on internal connectivity.
## Task 3. Explore the connectivity between VM instances
Explore the connectivity between the VM instances. Specifically, determine the effect of having VM instances in the same zone versus having instances in the same VPC network.
### Ping the external IP addresses
Ping the external IP addresses of the VM instances to determine if you can reach the instances from the public internet.
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
2. Note the external IP addresses for mynet-eu-vm, managementnet-us-vm, and privatenet-us-vm.
3. For mynet-us-vm, click SSH to launch a terminal and connect.
4. To test connectivity to mynet-eu-vm's external IP, run the following command, replacing mynet-eu-vm's external IP:
ping -c 3 <Enter mynet-eu-vm's external IP here>
Copied!
This should work!
To test connectivity to managementnet-us-vm's external IP, run the following command, replacing managementnet-us-vm's external IP:
ping -c 3 <Enter managementnet-us-vm's external IP here>
Copied!
This should work!
To test connectivity to privatenet-us-vm's external IP, run the following command, replacing privatenet-us-vm's external IP:
ping -c 3 <Enter privatenet-us-vm's external IP here>
Copied!
This should work!
Note: You are able to ping the external IP address of all VM instances, even though they are either in a different zone or VPC network. This confirms public access to those instances is only controlled by the ICMP firewall rules that you established earlier.
### Ping the internal IP addresses
Ping the internal IP addresses of the VM instances to determine if you can reach the instances from within a VPC network.
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
2. Note the internal IP addresses for mynet-eu-vm, managementnet-us-vm, and privatenet-us-vm.
3. Return to the SSH terminal for mynet-us-vm.
4. To test connectivity to mynet-eu-vm's internal IP, run the following command, replacing mynet-eu-vm's internal IP:
ping -c 3 <Enter mynet-eu-vm's internal IP here>
Copied!
Note: You are able to ping the internal IP address of mynet-eu-vm because it is on the same VPC network as the source of the ping (mynet-us-vm), even though both VM instances are in separate zones, regions and continents!
To test connectivity to managementnet-us-vm's internal IP, run the following command, replacing managementnet-us-vm's internal IP:
ping -c 3 <Enter managementnet-us-vm's internal IP here>
Copied!
Note: This should not work as indicated by a 100% packet loss!
To test connectivity to privatenet-us-vm's internal IP, run the following command, replacing privatenet-us-vm's internal IP:
ping -c 3 <Enter privatenet-us-vm's internal IP here>
Copied!
Note: This should not work either as indicated by a 100% packet loss! You are unable to ping the internal IP address of managementnet-us-vm and privatenet-us-vm because they are in separate VPC networks from the source of the ping (mynet-us-vm), even though they are all in the same zone us-east1.
VPC networks are by default isolated priv
VPC networks are by default isolated private networking domains. However, no internal IP address communication is allowed between networks, unless you set up mechanisms such as VPC peering or VPN.Task 4. Create a VM instance with multiple network interfaces
Every instance in a VPC network has a default network interface. You can create additional network interfaces attached to your VMs. Multiple network interfaces enable you to create configurations in which an instance connects directly to several VPC networks (up to 8 interfaces, depending on the instance's type).
### Create the VM instance with multiple network interfaces
Create the vm-appliance instance with network interfaces in privatesubnet-us, managementsubnet-us and mynetwork. The CIDR ranges of these subnets do not overlap, which is a requirement for creating a VM with multiple network interface controllers (NICs).
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
2. Click Create instance.
3. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Name	vm-appliance
Region	us-east1
Zone	<filled in at lab start>
Series	E2
Machine type	e2-standard-4

Note: The number of interfaces allowed in an instance is dependent on the instance's machine type and the number of vCPUs. The e2-standard-4 allows up to 4 network interfaces. Refer to the Maximum number of network interfaces section of the Google Cloud Guide for more information.
1. From Advanced options, click Networking, Disks, Security, Management, Sole-tenancy dropdown.
2. Click Networking.
3. For Network interfaces, click the dropdown to edit.
4. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Network	privatenet
Subnetwork	privatesubnet-us

1. Click Done.
2. Click Add network interface.
3. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Network	managementnet
Subnetwork	managementsubnet-us

1. Click Done.
2. Click Add network interface.
3. Set the following values, leave all other values at their defaults:
Property	Value (type value or select option as specified)
Network	mynetwork
Subnetwork	mynetwork

1. Click Done.
2. Click Create.
#### Test Completed Task
Click Che
### Explore the network interface details
Explore the network interface details of vm-appliance within the Cloud Console and within the VM's terminal.
1. In the Cloud Console, navigate to Navigation menu () > Compute Engine > VM instances.
2. Click nic0 within the Internal IP address of vm-appliance to open the Network interface details page.
3. Verify that nic0 is attached to privatesubnet-us, is assigned an internal IP address within that subnet (172.16.0.0/24), and has applicable firewall rules.
4. Click nic0 and select nic1.
5. Verify that nic1 is attached to managementsubnet-us, is assigned an internal IP address within that subnet (10.130.0.0/20), and has applicable firewall rules.
6. Click nic1 and select nic2.
7. Verify that nic2 is attached to mynetwork, is assigned an internal IP address within that subnet (10.128.0.0/20), and has applicable firewall rules.
Note: Each network interface has its own internal IP address so that the VM instance can communicate with those networks.
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
2. For vm-appliance, click SSH to launch a terminal and connect.
3. Run the following, to list the network interfaces within the VM instance:
sudo ifconfig
Copied!
The outpu
### Explore the network interface connectivity
Demonstrate that the vm-appliance instance is connected to privatesubnet-us, managementsubnet-us and mynetwork by pinging VM instances on those subnets.
1. In the Cloud Console, navigate to Navigation menu > Compute Engine > VM instances.
2. Note the internal IP addresses for privatenet-us-vm, managementnet-us-vm, mynet-us-vm, and mynet-eu-vm.
3. Return to the SSH terminal for vm-appliance.
4. To test connectivity to privatenet-us-vm's internal IP, run the following command, replacing privatenet-us-vm's internal IP:
ping -c 3 <Enter privatenet-us-vm's internal IP here>
Copied!
This works!
Repeat the same test by running the following:
ping -c 3 privatenet-us-vm
Copied!
Note: You are able to ping privatenet-us-vm by its name because VPC networks have an internal DNS service that allows you to address instances by their DNS names rather than their internal IP addresses. When an internal DNS query is made with the instance hostname, it resolves to the primary interface (nic0) of the instance. Therefore, this only works for privatenet-us-vm in this case.
To test connectivity to managementnet-us-vm's internal IP, run the following command, replacing managementnet-us-vm's internal IP:
ping -c 3 <Enter managementnet-us-vm's internal IP here>
Copied!
This works!
To test connectivity to mynet-us-vm's internal IP, run the following command, replacing mynet-us-vm's internal IP:
ping -c 3 <Enter mynet-us-vm's internal IP here>
Copied!
This works!
To test connectivity to mynet-eu-vm's internal IP, run the following command, replacing mynet-eu-vm's internal IP:
ping -c 3 <Enter mynet-eu-vm's internal IP here>
Copied!
Note: This does not work! In a multiple interface instance, every interface gets a route for the subnet that it is in. In addition, the instance gets a single default route that is associated with the primary interface eth0. Unless manually configured otherwise, any traffic leaving an instance for any destination other than a directly connected subnet will leave the instance via the default route on eth0.
To list the routes for vm-appliance instance, run the following command:
ip route
Copied!
The output should look like this:
default via 172.16.0.1 dev eth0
10.128.0.0/20 via 10.128.0.1 dev eth2
10.128.0.1 dev eth2 scope link
10.130.0.0/20 via 10.130.0.1 dev eth1
10.130.0.1 dev eth1 scope link
172.16.0.0/24 via 172.16.0.1 dev eth0
172.16.0.1 dev eth0 scope link
Note: The primary interface eth0 gets the default route (default via 172.16.0.1 dev eth0), and all three interfaces eth0, eth1 and eth2 get routes for their respective subnets. Since, the subnet of mynet-eu-vm (10.132.0.0/20) is not included in this routing table, the ping to that instance leaves vm-appliance on eth0 (which is on a different VPC network). You could change this behavior by configuring policy routing as documented in the Configuring policy routing section of the Google Cloud Guide.
## Congratulations!
In this lab you created a VM instance with three network interfaces and verified internal connectivity for VM instances that are on the subnets that are attached to the multiple interface VM.

https://www.cloudskillsboost.google/course_sessions/2617047/labs/344871
# Configuring an HTTP Load Balancer with Google Cloud Armor
## Overview
Google Cloud HTTP(S) load balancing is implemented at the edge of Google's network in Google's points of presence (POP) around the world. User traffic directed to an HTTP(S) load balancer enters the POP closest to the user and is then load-balanced over Google's global network to the closest backend that has sufficient capacity available.
Google Cloud Armor IP deny/allow rules enable you to restrict or allow access to your HTTP(S) load balancer at the edge of the Google Cloud, as close as possible to the user and to malicious traffic. This prevents malicious users or traffic from consuming resources or entering your virtual private cloud (VPC) networks.
In this lab, you will configure an HTTP load balancer with global backends, as shown in the diagram below. Then you stress test the load balancer and deny the stress test IP with Google Cloud Armor.

### Objectives
In this lab, you will learn how to perform the following tasks:
- Create a health check firewall rule
- Create two regional NAT configurations using Cloud Router
- Configure two instance templates
- Create two managed instance groups
- Configure an HTTP load balancer with IPv4 and IPv6
- Stress test an HTTP load balancer
- Deny an IP address to restrict access to an HTTP load balancer

Setup and requirements
## Task 1. Configure a health check firewall rule
Health checks determine which instances of a load balancer can receive new connections. For HTTP load balancing, the health check probes to your load-balanced instances come from addresses in the ranges 130.211.0.0/22 and 35.191.0.0/16. Your firewall rules must allow these connections.
### Create the health check rule
Create a firewall rule to allow health checks.
1. In the Cloud Console, in the Navigation menu (), select VPC network > Firewall.
   Notice the existing ICMP, internal, RDP, and SSH firewall rules.
  Each Google Cloud project starts with the default network and these firewall rules.
2. Click Create Firewall Rule.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Name	fw-allow-health-checks
Network	default
Targets	Specified target tags
Target tags	allow-health-checks
Source filter	IPV4 Ranges
Source IPV4 ranges	130.211.0.0/22 and 35.191.0.0/16
Protocols and ports	Specified protocols and ports

Note: Make sure to include the /22 and /16 in the Source IP ranges.
1. Select tcp and specify port 80.
2. Click Create.
Click Chec
## Task 2. Create two NAT configurations using Cloud Router
The Google Cloud VM backend instances that you set up in task 3 will not be configured with external IP addresses.
Instead, you will set up the Cloud NAT service to allow these VM instances to make outbound requests in order to install Apache Web server and PHP when they are launched. You create a Cloud Router for each managed instance group, one in us-central1 and one in the europe-west1 region, which you will configure in the next task.
### Create the Cloud Router instance
1. In the Cloud Console, in the Navigation menu (), select Network services > Cloud NAT.
2. Click Get started.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Gateway name	nat-usa
Network	default
Region	us-central1

1. Click Cloud Router and select Create new router.
2. For Name, type nat-router-us-central1.
3. Click Create.
4. In Create a cloud NAT gateway, click Create.
Note: Wait until the NAT Gateway Status changes to Running before moving onto the next task.
Repeat the same procedure for nat-europe.
1. Click Create Cloud NAT Gateway.
2. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Gateway name	nat-europe
Network	default
Region	europe-west1
Cloud Router > Create new router	Specify the name nat-router-europe-west1

1. Click Create.
2. In Create a NAT gateway, click Create.
Click Check
## Task 3. Configure an instance template and create instance groups
A managed instance group uses an instance template to create a group of identical instances. You will use these to create the backends of the HTTP load balancer.
### Configure the instance template
An instance template is an API resource that you can use to create VM instances and managed instance groups. Instance templates define the machine type, boot disk image, subnet, labels, and other instance properties.
1. In the Cloud Console, in the Navigation menu (), select Compute Engine > Instance templates.
2. Click Create instance template.
3. For Name, type us-central1-template.
4. Click Networking, disks, security, Management, sole tenancy.
5. Click Management.
6. Under Metadata, click + ADD ITEM and specify the following:
Key	Value
startup-script-url	gs://cloud-training/gcpnet/httplb/startup.sh

Note: The startup-script-url specifies a script that will be executed when instances are started. This script installs Apache and changes the welcome page to include the client IP and the name, region, and zone of the VM instance. You can find out more about this script by referring to the script reference guide.
1. Click Networking.
2. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Network tags	allow-health-checks
Network interface > Network	default
Subnetwork	default (us-central1)
External IP	None

Click DONE.
Note: The network tag allow-health-checks ensures that the Health Check firewall rule applies to these instances.
1. Click Create. Wait for the instance template to be created.
2. Now, prepare to create another instance template by copying us-central1-template. Click the us-central1-template. Information about the us-central1-template appears.
3. Near the top of the page, click CREATE SIMILAR.
4. For Name, type europe-west1-template.
5. Click Networking, disks, security, Management, sole tenancy.
6. Click Networking > Network interface.
7. Select default (europe-west1) as the Subnetwork, and click DONE.
8. Click Create.
### Create the managed instance groups
Create a managed instance group in us-central1 and one in europe-west1.
1. In the Navigation menu, select Compute Engine > Instance groups.
2. Click Create Instance group.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Name	us-central1-mig
Location	Multiple zones
Region	us-central1
Instance template	us-central1-template
Autoscaling > Autoscaling metrics	Click CPU utilization, set Target CPU utilization 80
Cool-down period	45
Minimum number of instances	1
Maximum number of instances	5

Note: Managed instance groups offer autoscaling capabilities that allow you to automatically add or remove instances from a managed instance group based on increases or decreases in load. Autoscaling helps your applications gracefully handle increases in traffic and reduces cost when the need for resources is lower. You just define the autoscaling policy, and the autoscaler performs automatic scaling based on the measured load.
1. Click Create.
  Repeat the same procedure for europe-west1-mig in europe-west1.
2. Click Create Instance group.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Name	europe-west1-mig
Location	Multiple zones
Region	europe-west1
Instance template	europe-west1-template
Autoscaling > Autoscaling metrics	Click CPU utilization, set Target CPU utilization 80
Cool-down period	45
Minimum number of instances	1
Maximum number of instances	5

Click Create.
Click Check
### Verify the backends
Verify that VM instances are being created in both regions and access their HTTP sites.
1. In the Navigation menu, click Compute Engine > VM instances.
   Notice the instances that start with us-central1-mig and europe-west1-mig.
  These instances are part of the managed instance groups.
2. In Cloud Console, note the name and the zone of the VM instance located in Europe. (You will need to use these values in a moment.)
3. On the Google Cloud Platform menu, click Activate Cloud Shell () to open Cloud Shell. If prompted, click Continue.
4. In Cloud Shell, execute this command to execute SSH commands in the VM instance located in Europe:
gcloud compute ssh <INSTANCE_NAME> --zone <ZONE>
Copied!
1. If prompted, click Authorize.
2. When asked if you want to continue, enter Y.
3. When prompted for a passphrase, press Enter or Return. This will generate an empty passphrase.
4. To confirm the empty passphrase, press Enter or Return again. After a moment, Cloud Shell uses IAP tunneling to make an SSH connection to the VM instance in Europe. The Cloud Shell command line can now be used as the VM instance's command line.
5. At the command line, enter the following:
curl localhost
Copied!
You should see the Apache welcome page, which was installed as part of the startup-script-url script that changes the welcome page to include the client IP and the name, region, and zone of the VM instance.
1. Copy the internal IP address of an instance located in the us-central region.
2. Test the connection by running the following command:
curl $IP_Address
Copied!
Note: Replace the value $IP_Address with the internal IP of the us-central1 instance.
Enter exit to close the SSH session.
## Task 4. Configure the HTTP load balancer
Next, you will configure the HTTP load balancer to balance traffic between the two backends (us-central1-mig in us-central1 and europe-west1-mig in europe-west1), as illustrated in the network diagram.

### Start the configuration
1. In the Navigation menu, select Network Services > Load balancing.
2. Click Create load balancer.
3. Under HTTP(S) Load Balancing, click Start configuration.
4. Select From Internet to my VMs or serverless services.
5. From Global or Regional, select Global HTTP(S) Load Balancer (classic) and click Continue.
6. For Name, type http-lb.
### Configure the backend
Backend services direct incoming traffic to one or more attached backends. Each backend is composed of an instance group and additional serving capacity metadata.
1. Click Backend configuration.
2. For Backend services & backend buckets, click Create a backend service.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (select option as specified)
Name	http-backend
Backend type	Instance group
Instance group	us-central1-mig
Port numbers	80
Balancing mode	Rate
Maximum RPS	50
Capacity	100

Note: This configuration means that the load balancer attempts to keep each instance of us-central1-mig at or below 50 requests per second (RPS).
1. Click Done.
2. Click Add backend.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (select option as specified)
Instance group	europe-west1-mig
Port numbers	80
Balancing mode	Utilization
Maximum backened utilization	80
Capacity	100

Note: This configuration means that the load balancer attempts to keep each instance of europe-west1-mig at or below 80% CPU utilization.
1. Click Done.
2. For Health Check, select Create a health check.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (select option as specified)
Name	http-health-check
Protocol	TCP
Port	80

Note: Health checks determine which instances can receive new connections. This HTTP health check polls instances every 10 seconds, waits up to 5 seconds for a response, and treats 2 successful or 3 failed attempts as healthy or unhealthy, respectively.
1. Click Save.
2. Check the Enable Logging box.
3. Set the Sample Rate to 1.
4. Click Create.
### Configure the frontend
The host and path rules determine how your traffic will be directed. For example, you could direct video traffic to one backend and direct static traffic to another backend. However, you are not configuring the host and path rules in this lab.
1. Click Frontend configuration.
2. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Protocol	HTTP
IP version	IPv4
IP address	Ephemeral
Port	80

1. Click Done.
2. Click Add Frontend IP and port.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Protocol	HTTP
IP version	IPv6
IP address	Ephemeral
Port	80

Click Done.
Note: HTTP(S) load balancing supports both IPv4 and IPv6 addresses for client traffic. Client IPv6 requests are terminated at the global load balancing layer and then proxied over IPv4 to your backends.
### Review and create the HTTP load balancer
1. Click Review and finalize.
2. Review the Backend services and Frontend.
3. Click Create.
   Wait for the load balancer to be created.
4. Click on the name of the load balancer (http-lb).
5. Note the IPv4 and IPv6 addresses of the load balancer for the next task. They will be referred to as [LB_IP_v4] and [LB_IP_v6], respectively.
Note: The IPv6 address is the one in hexadecimal format.
Click Chec
## Task 5. Test the HTTP load balancer
Now that you have created the HTTP load balancer for your backends, it is time to verify that traffic is forwarded to the backend service.
### Access the HTTP load balancer
Open a new tab in your browser and navigate to http://[LB_IP_v4]. Make sure to replace [LB_IP_v4] with the IPv4 address of the load balancer.
Note: It might take a couple of minutes to access the HTTP load balancer. In the meantime, you might get a 404 or 502 error. Keep trying until you see the page of one of the backends.Note: Depending on your proximity to us-central1 and europe-west1, you traffic is either forwarded to a us-central1-mig or europe-west1-mig instance.
If you have a local IPv6 address, try the IPv6 address of the HTTP load balancer by navigating to http://[LB_IP_v6]. Make sure to replace [LB_IP_v6] with the IPv6 address of the load balancer.
### Stress test the HTTP load balancer
Next, you will create a new VM to simulate a load on the HTTP load balancer. Then you will determine whether traffic is balanced across both backends when the load is high.
1. In the Cloud Console, in the Navigation menu (), select Compute Engine > VM instances.
2. Click Create instance.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Name	siege-vm
Region	us-west1
Zone	us-west1-c

Note: Because us-west1 is closer to us-central1 than to europe-west1, traffic should be forwarded only to us-central1-mig (unless the load is too high).
1. Click Create. Wait for the siege-vm instance to be created.
2. At the Cloud Shell prompt, enter the following command to create an SSH connection to the siege-vm:
gcloud compute ssh siege-vm --zone us-west1-c
Copied!
Run the following command to install siege:
sudo apt-get -y install siege
Copied!
To store the IPv4 address of the HTTP load balancer in an environment variable, run the following command, replacing [LB_IP_v4] with the IPv4 address:
export LB_IP=[LB_IP_v4]
Copied!
Verify it with echo:
echo $LB_IP
Copied!
To simulate a load, run the following command:
siege -c 250 http://$LB_IP
Copied!
The output should look like this.
Output:
New configuration template added to /home/cloudcurriculumdeveloper/.siege
Run siege -C to view the current settings in that file
[alert] Zip encoding disabled; siege requires zlib support to enable it: No such file or directory
** SIEGE 4.0.2
** Preparing 250 concurrent users for battle.
The server is now under siege...
1. In the Cloud Console, in the Navigation menu (), select Network Services > Load balancing.
2. Click http-lb.
3. Click Monitoring.
4. Monitor the Frontend Location (Total inbound traffic) between North America and the two backends for 2 to 3 minutes.
5. Return to the SSH terminal of siege-vm.
6. Press CTRL+C to stop siege.
## Task 6. Deny the siege-vm
You will now use Google Cloud Armor to deny the siege-vm from accessing the HTTP load balancer.
### Create the security policy
Create a Google Cloud Armor security policy with a deny rule for the siege-vm.
1. In the Cloud Console, in the Navigation menu, select Compute Engine > VM instances.
2. Note the External IP of the siege-vm. This will be referred to as [SIEGE_IP].
Note: There are ways to identify the external IP address of a client trying to access your HTTP load balancer. For example, you could examine traffic captured by VPC Flow Logs in BigQuery to determine a high volume of incoming requests.
1. In the Navigation menu, select Network Security > Cloud Armor.
2. Click Create policy.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Name	deny-siege
Default rule action	Allow

1. Click Next step.
2. Click Add rule.
3. Specify the following, and leave the remaining settings as their defaults:
Property	Value (type value or select option as specified)
Condition > Match	Enter the SIEGE_IP
Action	Deny
Deny status	403 (Forbidden)
Priority	1000

1. Click Done.
2. Click Next step.
3. Click Add Target.
4. For Type, select Load balancer backend service.
5. For Target, select http-backend.
6. Click Create policy.
   Wait for the policy to be created before moving to the next step.
Note: Alternatively, you could set the default rule to Deny and only allow traffic from authorized users/IP addresses.
Click Che
### Verify the security policy
Next, you will verify that the siege-vm cannot access the HTTP load balancer.
1. Return to the SSH terminal of siege-vm.
2. To access the load balancer, run the following:
curl http://$LB_IP
Copied!
The output should look like this.
Output:
<!doctype html><meta charset="utf-8"><meta name=viewport content="width=device-width, initial-scale=1"><title>403</
title>403 Forbidden
Note: It might take a couple of minutes for the security policy to take affect. If you are able to access the backends, keep trying until you get the 403 Forbidden error.
Open a new tab in your browser and navigate to http://[LB_IP_v4]. Make sure to replace [LB_IP_v4] with the IPv4 address of the load balancer.
Note: You can access the HTTP load balancer from your browser because of the default rule to allow traffic; however, you cannot access it from the siege-vm because of the deny rule that you implemented.
To simulate a load, run the following command:
siege -c 250 http://$LB_IP
Copied!
The output should look like this.
Output:
[alert] Zip encoding disabled; siege requires zlib support to enable it
** SIEGE 4.0.2
** Preparing 250 concurrent users for battle.
The server is now under siege...
Explore the security policy logs to determine whether this traffic is also blocked.
1. In the Cloud Console, in the Navigation menu, select Network Security > Cloud Armor.
2. Click deny-siege.
3. Click Logs.
4. Click View policy logs. Logs Explorer is launched. You should see the logs for the http-lb load balancer.
5. Expand a log entry in Query results.
6. Expand httpRequest.
The request should be from the siege-vm IP address. If not, expand another log entry.
1. Expand jsonPayload.
2. Expand enforcedSecurityPolicy.
   Notice that the configuredAction is to DENY with the name deny-siege.
Note: Google Cloud Armor security policies create logs that can be explored to determine when traffic is denied and when it is allowed, along with the source of the traffic.
## Congratulations!
In this lab, you have configured an HTTP load balancer with backends in us-central1 and europe-west1. Then you stress-tested the load balancer with a VM and denied the IP address of that VM with Google Cloud Armor. In addition, you were able to explore the security policy logs to identify why the traffic was blocked.
Aulas
aulas
aulas

https://www.cloudskillsboost.google/course_sessions/2617047/labs/344880
# Cloud Monitoring: Qwik Start

## Overview
Cloud Monitoring provides visibility into the performance, uptime, and overall health of cloud-powered applications. Cloud Monitoring collects metrics, events, and metadata from Google Cloud, Amazon Web Services, hosted uptime probes, application instrumentation, and a variety of common application components including Cassandra, Nginx, Apache Web Server, Elasticsearch, and many others. Cloud Monitoring ingests that data and generates insights via dashboards, charts, and alerts. Cloud Monitoring alerting helps you collaborate by integrating with Slack, PagerDuty, HipChat, Campfire, and more.
This hands-on lab shows you how to monitor a Compute Engine virtual machine (VM) instance with Cloud Monitoring. You'll also install monitoring and logging agents for your VM which collects more information from your instance, which could include metrics and logs from 3rd party apps.
## Task 1. Create a Compute Engine instance
1. In the Cloud Console dashboard, go to Navigation menu > Compute Engine > VM instances, then click Create instance.
2. Fill in the fields as follows, leaving all other fields at the default value:
Field	Value
Name	lamp-1-vm
Region	us-central1
Zone	us-central1-a
Series	N1
Machine type	n1-standard-2
Boot disk	Click Change. Select version Debian GNU/Linux 10 (buster) for Debian OS and click Select.
Firewall	check Allow HTTP traffic

Click Create.
Wait a couple of minutes, you'll see a green check when the instance has launched.
Click Chec
## Task 2. Add Apache2 HTTP Server to your instance
1. In the Console, click SSH in line with lamp-1-vm to open a terminal to your instance.
2. Run the following commands in the SSH window to set up Apache2 HTTP Server:
sudo apt-get update
Copied!
sudo apt-get install apache2 php7.0
Copied!
When asked if you want to continue, enter Y.
Note: If you cannot install php7.0, use php5.
sudo service apache2 restart
Copied!
Click Chec
Return to the Cloud Console, on the VM instances page. Click the External IP for lamp-1-vm instance to see the Apache2 default page for this instance.
Click Check my p
Create a Monitoring Metrics Scope
Set up a Monitoring Metrics Scope that's tied to your Google Cloud Project. The following steps create a new account that has a free trial of Monitoring.
In the Cloud Console, click Navigation menu  > Monitoring.
When the Monitoring Overview page opens, your metrics scope project is ready.
### Install the Monitoring and Logging agents
Agents collect data and then send or stream info to Cloud Monitoring in the Cloud Console.
The Cloud Monitoring agent is a collected-based daemon that gathers system and application metrics from virtual machine instances and sends them to Monitoring. By default, the Monitoring agent collects disk, CPU, network, and process metrics. Configuring the Monitoring agent allows third-party applications to get the full list of agent metrics. On the Google Cloud, Operations website, see Cloud Monitoring Documentation for more information.
In this section, you install the Cloud Logging agent to stream logs from your VM instances to Cloud Logging. Later in this lab, you see what logs are generated when you stop and start your VM.
Note: It is best practice to run the Cloud Logging agent on all your VM instances.
Run the Monitoring agent install script command in the SSH terminal of your VM instance to install the Cloud Monitoring agent:
curl -sSO https://dl.google.com/cloudagents/add-google-cloud-ops-agent-repo.sh
Copied!
sudo bash add-google-cloud-ops-agent-repo.sh --also-install
Copied!
1. When asked if you want to continue, enter Y.
2. Run the Logging agent install script command in the SSH terminal of your VM instance to install the Cloud Logging agent:
sudo systemctl status google-cloud-ops-agent"*"
Copied!
Enter q to exit the status.
sudo apt-get update
Copied!
## Task 3. Create an uptime check
Uptime checks verify that a resource is always accessible. For practice, create an uptime check to verify your VM is up.
1. In the Cloud Console, in the left menu, click Uptime checks, and then click +Create Uptime Check.
2. Set the following fields:
Title: Lamp Uptime Check, then click Next.
Protocol: HTTP
Resource Type: Instance
Applies to: Single, lamp-1-vm
Path: leave at default
Check Frequency: 1 min, then click Next.
1. Click Next to leave the Response Validation details to default. Click Test to verify that your uptime check can connect to the resource.
2. When you see a green check mark everything can connect. Click Create.
The uptime check you configured takes a while for it to become active. Continue with the lab, you'll check for results later. While you wait, create an alerting policy for a different resource.
## Task 4. Create an alerting policy
Use Cloud Monitoring to create one or more alerting policies.
1. In the left menu, click Alerting, and then click +Create Policy.
2. Click on Select a metric dropdown. Disable the Show only active resources & metrics.
3. Type Network traffic in filter by resource and metric name and click on VM instance > Interface. Select Network traffic (agent.googleapis.com/interface/traffic) and click Apply. Leave all other fields at the default value.
4. Click Next.
5. Set the Threshold position to Above threshold, Threshold value to 500 and Advanced Options > Retest window to 1 min. Click Next.
6. Click on the drop down arrow next to Notification Channels, then click on Manage Notification Channels.
A Notification channels page will open in a new tab.
1. Scroll down the page and click on ADD NEW for Email.
2. In the Create Email Channel dialog box, enter your personal email address in the Email Address field and a Display name.
3. Click on Save.
4. Go back to the previous Create alerting policy tab.
5. Click on Notification Channels again, then click on the Refresh icon to get the display name you mentioned in the previous step.
6. Click on Notification Channels again if necessary, select your Display name and click OK.
7. Add a message in documentation, which will be included in the emailed alert.
8. Mention the Alert name as Inbound Traffic Alert.
9. Click Next.
10. Review the alert and click Create Policy.
You've created an alert! While you wait for the system to trigger an alert, create a dashboard and chart, and then check out Cloud Logging.
Click Che
## Task 5. Create a dashboard and chart
You can display the metrics collected by Cloud Monitoring in your own charts and dashboards. In this section you create the charts for the lab metrics and a custom dashboard.
1. In the left menu select Dashboards, and then +Create Dashboard.
2. Name the dashboard Cloud Monitoring LAMP Qwik Start Dashboard.
### Add the first chart
1. Click the Line option in the Chart library.
2. Name the chart title CPU Load.
3. Click on Resource & Metric dropdown. Disable the Show only active resources & metrics.
4. Type CPU load (1m) in filter by resource and metric name and click on VM instance > Cpu. Select CPU load (1m) and click Apply. Leave all other fields at the default value. Refresh the tab to view the graph.
### Add the second chart
1. Click + Add Chart and select Line option in the Chart library.
2. Name this chart Received Packets.
3. Click on Resource & Metric dropdown. Disable the Show only active resources & metrics.
4. Type Received packets in filter by resource and metric name and click on VM instance > Instance. Select Received packets and click Apply. Refresh the tab to view the graph.
5. Leave the other fields at their default values. You see the chart data.
## Task 6. View your logs
Cloud Monitoring and Cloud Logging are closely integrated. Check out the logs for your lab.
1. Select Navigation menu > Logging > Logs Explorer.
2. Select the logs you want to see, in this case, you select the logs for the lamp-1-vm instance you created at the start of this lab:
- Click on Resource.
- Select VM Instance > lamp-1-vm in the Resource drop-down menu.
- Click Apply.
- Leave the other fields with their default values.
- Click the Stream logs.
You see the logs for your VM instance.
### Check out what happens when you start and stop the VM instance.
To best see how Cloud Monitoring and Cloud Logging reflect VM instance changes, make changes to your instance in one browser window and then see what happens in the Cloud Monitoring, and then Cloud Logging windows.
1. Open the Compute Engine window in a new browser window. Select Navigation menu > Compute Engine, right-click VM instances > Open link in new window.
2. Move the Logs Viewer browser window next to the Compute Engine window. This makes it easier to view how changes to the VM are reflected in the logs
3. In the Compute Engine window, select the lamp-1-vm instance, click the three vertical dots at the right of the screen and then click Stop, and then confirm to stop the instance.
It takes a few minutes for the instance to stop.
1. Watch in the Logs View tab for when the VM is stopped.
2. In the VM instance details window, click the three vertical dots at the right of the screen and then click Start/resume, and then confirm. It will take a few minutes for the instance to re-start. Watch the log messages to monitor the start up.
## Task 7. Check the uptime check results and triggered alerts
In the Cloud Logging window, select Navigation menu > Monitoring > Uptime checks. This view provides a list of all active uptime checks, and the status of each in different locations.
You will see Lamp Uptime Check listed. Since you have just restarted your instance, the regions are in a failed status. It may take up to 5 minutes for the regions to become active. Reload your browser window as necessary until the regions are active.
Click the name of the uptime check, Lamp Uptime Check.
Since you have just restarted your instance, it may take some minutes for the regions to become active. Reload your browser window as necessary.
### Check if alerts have been triggered
1. In the left menu, click Alerting.
2. You see incidents and events listed in the Alerting window.
3. Check your email account. You should see Cloud Monitoring Alerts.
Note: Remove the email notification from your alerting policy. The resources for the lab may be active for a while after you finish, and this may result in a few more email notifications getting sent out.
## Congratulations!
You have